Smartflow M4 V3 Bootloader

# Hardware
Processor:SAMD51J19A
Bootloader size TBC ~60Kb
Fuses: TBC
Modem:SIM868 – making use of the built in ftp functionality to transfer files down

Template Bootloaders:
samdx1_sam_ba – traditional Bootloader ( adafruit\samd\bootloaders\metroM4)
Storage:SPI flash Winbond 25Q16 as per the Metro M4

## Fuses
The booloader can set the fuses to known values to help production and unlocking of devices if needed

## Flash Storage
SPI flash Winbond 25Q16 as used on the Metro M4

The following data must be stored in the spi flash for the bootloader to work:
- 12 digit serial number
- 16 char ascii string for hardware version “smarflow3v00”

Additonal Data will be stored in the SPI flash memory:

MainProgramChecksum : 32 bits – this is used to check if the main program is good to run

## Bootloader File Format
The main file will be named after the hardware version - “smarflow3v00.bin”
An info file will also exsist to aid the bootloader - “smarflow3v00.bdf”.

The .bdf file will have blocks of data to help the Bootloader:
BinFileName 16 char ascii string
BinFileSize 32 bits
BinFileStartAddress 32 bits
BinFileUserWords[4] 32 bits
BinFileChecksum 32 bits
BinFileBlockSize 32 bits
BinFileBlockNumberBlocks[] 32 Bits
BdfFileChecksum

Size of a programming Block is deteremined by:
GSM – amount of data that can be easily moved over gprs
SPI flash Block Size

The checksums will be same style reported in the main program - 32 bit 2’s complement
# Bootloader Build System
Need to check if the Adafruit Usb Storage
We may have to use Arduino code to drive the SPI flash

# Bootloader Operation:

# Ftp_Bootloader_Start:

### Precheck
We need Network to be good before we can start – if we dont have it and we where forced to try we will have to postpone it – see failure modes

## Main Check
Bypass link will be checked – if present Goto_Main_App

The modem will be turned on now

Check “Force Update Static RAM location” – if force active then go to Ftp_Bootloader_Start ( FLAG_APP_FORCE)

Check if the main program is valid – if not (invalid checksum) Ftp_Bootloader_Start (FLAG_APP_INVALID)

Check if sim card installed – if not Goto_Main_App

Check “RTC Last Update Time” – if the version has been checked recently then Goto_Main_App

### BDF Check Process
The Bootloader will connect to an FTP server using PORT mode (no pasv support)

It will download the bdf file based on the hardware name comprised of the hardware version + .dat for example “smartflow3v00.bdf”

It will use the data in the file to quickly check if Main App needs updated

See “Bootloader File Format”

If there is no need to udpate then Goto_Main_App – using the main checksum

Bdf Verification

Check the BdfFileChecksum is valid

Use the FTP command to check the reported size of the bin file against the bdf.BinFileName & bdf.BinFileSize information

## Bin Block Download Process

A FTP transfer will begin – broken down into blocks of data to suit GSM transport ~ 256 bytes

### Notes
Failure modes can occur such as:
- no sim card
- Bad recepetion – cannot register
- Cannot connect to ftp server
- no dat / invalid file
- no bin file
- Cannot complete a download ( perhaps bad reception during download or server failure)
- checksum failure of downloaded data

# GoTo_Main_App

Vector to the main program – passing all control to the main App – no more checks

## Check Limting
The bootloader should know the last time it checked for new version

Clock Source = RTC which was updated by the GSM time.
If the RTC is invalid it must check for an update.

This is to ensure the bootloader is not slowing down normal reboots

## Recovery Mode

### Bypass Mode
A link can be seen by the bootloader to the decide NOT to perform an update – this is for development as a the new flash code will be over-riden on next reboot

# General Operation
The Bootloader will connect to a FTP server and download its firmware

Ftp Login

User:MAC address (ascii string decimal chars x 12)
Password:IMEI of the SIM868 module TBC

### Notes
Could use email format as username to pass more data in
We want to use a FTP server as this functioanlity is built into the modems
We are using VSFTPD on EC2/AWS – it can be modified to pass a custom firmware to the device if needed.

Try and use as much